## Slide 1: Wireless for the Internet of Things IEEE 802.15.4 - Introduction
CS/ECE 4501
Spring 2023
UVA
[Pannuto, Ghena, Campbell]

## Slide 2: Today’s Goals
Introduce the IEEE 802.15.4 standard
  Specifically designed for low power applications
Overview of physical layer details
Exploration of link layer
  Network topologies
  Communication structure

## Slide 3: References
802.15.4 Specification [2006]
  “Part 15.4: Wireless Medium Access Control (MAC) and Physical Layer (PHY) Specifications for Low-Rate Wireless Personal Area Networks (WPANs)”
Other helpful references:
  Paper introducing the 802.15.4 draft
  NXP 802.15.4 Stack User Guide
  2005 presentation on 802.15.4

## Slide 4: Outline
Overview
Physical Layer
Link Layer

## Slide 5: Comparison of networks
Data
Throughput
Range

## Slide 6: Comparison of networks
Bluetooth
WiFi
Cellular
BLE
802.15.4
Data
Throughput
Range
LPWANs

## Slide 7: Comparison of networks
Bluetooth
WiFi
Cellular
BLE
802.15.4
Data
Throughput
Range
There are some missing qualities here. Why be closer to the origin?
LPWANs

## Slide 8: Comparison of networks
Bluetooth
WiFi
Cellular
BLE
802.15.4
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost
LPWANs

## Slide 9: IEEE 802….
Anyone heard “Eight-Oh-Two Dot” ?
  Where?
  What is it?

## Slide 10: IEEE 802
Network standards for variable-sized packets
  Ethernet
  WiFi
  WPANs
E.g. not networks that send periodic constant-sized packets
Specifies PHY and Link layers
Another example standard:
  IEEE 754: Floating Point

## Slide 11: IEEE 802.15
Wireless Personal-Area Networks (WPAN)
  All the things within the workspace of a person
  Conceptually smaller domain that the Local Area Network
  Realistically about the same thing as a LAN
Formerly included a Bluetooth spec
  Bluetooth SIG took over governance

## Slide 12: 802.15.4 (LR-WPANs) Overview “Low-Rate Wireless Personal Area Networks”
Goals
  “The IEEE 802.15 TG4 was chartered to investigate a low data rate solution with multi-month to multi-year battery life and very low complexity.” [TG4]
Applications
  “Potential applications are sensors, interactive toys, smart badges, remote controls, and home automation.” [TG4]
  Ultimately home automation, industrial control/monitoring, vehicular sensing, agriculture; really most machine-to-machine (M2M) sensor applications
Other contemporary technologies
  WiFi 802.11b and Bluetooth Classic
    Too complex in specification and overachieving in capability

## Slide 13: IEEE 802.15.4
Low-Rate Wireless PAN
  250 kbps, ~100 m range
  Radio hardware available with low-power and low-cost
Specification: 2003
  Also 2006, 2011, 2015, and 2020 revisions
    Mostly various added capabilities such as extra PHY layers
    Also define optional security, scheduling, and larger frame sizes
We’ll mostly work off of the 2006 version
  Thread is based on 2006 version
  Zigbee is based on the original 2003 version
  Roughly 200 pages of meaningful specification (100 of appendices)
    Compare to 3000 pages of Bluetooth/BLE

## Slide 14: Outline
Overview
Physical Layer
Link Layer

## Slide 15: 802.15.4 Physical Layers
Multiple options of physical layers are supported
  We’ll focus on 2.4 GHz (2400 MHz)

## Slide 16: Physical Layer
O-QPSK modulation
  Offset Quadrature Phase-Shift Keying
  Twice the data rate of BPSK for same BER
  Cost: most complicated design of receivers
    Which is pretty minimal with all the transistors we’ve got
    Plus the ability to reuse previous designs
  4 bits per symbol
Symbols versus bits
  A symbol is the unit of data transfer for a modulated signal
    Does not necessarily correspond 1:1 with bits
  The rate of symbols per second is a baudrate
802.15.4 bit rate at 2.4 GHz: 2000 kchips/s, which is 250 kbps, which is 62.5 kBaud
Notes: https://rfmw.em.keysight.com//wireless/helpfiles/n7610b/Content/Main/IEEE%20802.15.4%20ZigBee.htm

## Slide 17: 802.15.4 Modulation (@2.4 GHz fc) O-QPSK with half-sine shaping is MSK!
Notes: https://www.dsprelated.com/showarticle/1016.php – For reconvincing myself that yes, it really does boil down to MSK (Minimum Shift Keying) (a subset of FSK) on the air, which is insane.
https://arxiv.org/pdf/1611.03482.pdf – Also this for the same

## Slide 18
Input bit stream
Broken into 4-bit symbols
Each symbol maps to a 32-bit pseudo-noise code (PN-code) or sometimes pseudo-random sequence
Each bit of the PN code is called a chip
Each chip encodes half a sine wave
Chips alternate in-phase and quadrature
Quadrature component is offset π/2
I and Q half-sines are baseband, which are mixed with the carrier
I and Q carriers are combined to create the final on-air signal
Signal is MSK, which is a special, optimal case of FSK!
802.15.4 Modulation (@2.4 GHz fc) O-QPSK with half-sine shaping is MSK!
Notes: https://www.dsprelated.com/showarticle/1016.php – For reconvincing myself that yes, it really does boil down to MSK (minimal shift keying) (a subset of FSK) on the air, which is insane.
https://arxiv.org/pdf/1611.03482.pdf – Also this for the same

## Slide 19: O-QPSK results in continuous wave
Standard BPSK
O-QPSK (MSK)

## Slide 20: The magic of I and Q channels are that we get two dimensions
This is called a “constellation diagram”
  We’ll talk about these more with cellular
Notes: If digging into constellation, the M of MSK is the essence of not going 00<>11 or 01<>10, decoding is measuring which way around the circle you move (+ or – π/2)

## Slide 21: Why do we map symbols to chips?
We took the 4 bits we want to send…
… and sent 32 bits instead??
Why?

## Slide 22: Direct Sequence Spread Spectrum (DSSS)
Increases the signal bandwidth of a transmission beyond information bandwidth
  Send sequences of chips, which are a translation of one symbol to a pattern of many bits
  Chips are transmitted much faster than symbols, essentially increasing the data rate
Enables better interference avoidance
  Received bits are correlated against codes to see which is most likely
  802.15.4 tolerates 13-15 bit flips (almost half!)
Notes: n.b. 802.15.4 channels 5 MHz wide
BT Classic 1 MHz, BLE 2 MHz

## Slide 23: DSSS example
Data sent is 101
  Code is longer than data, so we replicate bits
  Data is recoverable, even with noise
https://circuitcellar.com/research-design-hub/dsss-in-a-nutshell/

## Slide 24: Show me the money: what is the actual data rate of 802.15.4 (2.4 GHz)?
Chip rate: 2000 kchips/sec
pollev.com/wiotbc

## Slide 25: 802.15.4 RF channels
27 channels across three bands
5 MHz channel separation at 2.4 GHz
  Compare to 2 MHz for BLE
  (or to 1 MHz for BT Classic)

## Slide 26: Regional bands
Different RF bands have different regional availability
Also have different rules
  915 MHz: 400 ms dwell time
  868 MHz: 1% duty cycle

## Slide 27: Signal strength
Transmit power
  Typical: 0 dBm (remember: 1 mW)
Receiver sensitivity
  nRF52840 802.15.4: -100 dBm
    Compare to BLE sensitivity of -95 dBm
  Minimum acceptable: -85 dBm
  Circa-2006 radios (CC2420): -95 dBm
Which has longer range, 802.15.4 or BLE? Why?
  802.15.4 with +5 dBm more margin; lower bit rate plays into this

## Slide 28: Outline
Overview
Physical Layer
Link Layer

## Slide 29: 802.15.4 network topologies
Only specifies PHY and MAC, but has use cases in mind

## Slide 30: Star and Tree topologies
PAN Coordinator
  Receives and relays all messages
  Most capable and power-intensive
Coordinators (a.k.a. Routers)
  Control “clusters”
  Receives and relays to its children
  Communicates up to parent coordinator
End Devices
  Only communicate with single parent coordinator
  Least capable and power intensive

## Slide 31: Mesh networks
Most devices are capable of communicating with multiple neighbors
What are advantages of mesh?
What are disadvantages of mesh?

## Slide 32: Mesh networks
Most devices are capable of communicating with multiple neighbors
What are advantages of mesh?
  Devices can communicate over longer distances
  Device failures less likely to collapse the entire network
What are disadvantages of mesh?
  Some nodes have to spend more energy communicating
  Network protocol becomes more complicated to manage routing

## Slide 33: Reminder: CSMA/CA Carrier Sense Multiple Access with Collision Avoidance
First, wait a random amount (collision avoidance part)
Then, listen for a duration and determine if anyone is transmitting (carrier sense part)
  If idle, you can transmit
  If busy, repeat step 1 (often increasing maximum wait time)
Can be combined with notion of slotting
  Synchronize to slots (smaller than transmit times)
  Wait for a number of slots
  Listen for idle slots

## Slide 34: Modes of operation
Beacon-enabled PAN
  Slotted CSMA/CA
  Structured communication patterns
  Optionally with some TDMA scheduled slots
Non-beacon-enabled PAN
  Unslotted CSMA/CA
  No particular structure for communication
    Could be defined by other specifications, like Thread or Zigbee

## Slide 35: Beacon-enabled superframe structure
Beacons occur periodically [15 ms – 245 seconds]
  Devices must listen to each beacon
Contention Access Period
  Slotted CSMA/CA synchronized by beacon start time
Inactive Period
  No communication occurring. Assumes sleepy devices
Contention Access Period
Beacon
Inactive Period
Beacon
…

## Slide 36: Guaranteed Time Slots (GTS)
PAN Coordinator may create a Contention Free Period with Guaranteed Time Slots
  TDMA schedule assigned to specific devices
  Slots eat up part of the Contention Access Period
  No CSMA/CA within a slot
Contention Access Period
Beacon
Inactive Period
Beacon
Guaranteed Time Slots
…

## Slide 37: Handling tree-based topologies
All coordinators listen to beacon from PAN coordinator
  And can participate in that contention period
Send their own beacons to leaf devices during inactive period
  Leaves participate in that contention period

## Slide 38: Non-beacon-enabled PAN
Same idea, just no beacons
  Which removes synchronization benefit (and slotted CSMA/CA)
  Also removes beacon listening cost
    Devices only need to check for activity before transmitting
  Still need an algorithm to determine when it should receive data
    All the time is a huge energy drain
    Algorithms can get complicated here
    Does BLE mechanism of listen-after-send apply?
      Only if sending to a high-power device, not among equals
Contention Access Period
…

## Slide 39: Receiving messages
Listen during entire contention period
  Can receive direct messages from any other device
  Can immediately respond to messages as well
Request messages from Coordinator
  Make all communication go through Coordinator
  Send a request-for-data packet to coordinator to get information
  Coordinator can include list of devices with pending data in beacon
More complicated listening algorithms are possible

## Slide 40: Clear Channel Assessment (CCA)
The “listen” part of CSMA/CA
Variety of implementations are acceptable
Energy above threshold
  Energy for 8 symbol durations above threshold (RSSI)
Carrier sense
  Valid 802.15.4 carrier signal
Energy AND/OR Carrier

## Slide 41: Slotted CSMA/CA operation
Have data to send
Wait for next backoff slot (synchronized from beacon)
Wait for 0-7 backoff slots (slot is 20 symbol durations: 320 us)
Listen for two empty slots
  Idle: Transmit
  Occupied: wait 0-15 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat (upper limit configurable)
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Timeout

## Slide 42: Unslotted CSMA/CA operation
Have data to send
Wait for next backoff slot (synchronized from beacon)
Wait for 0-7 backoff slots (slot is 20 symbol durations: 320 us)
Listen for two empty slots
  Idle: Transmit
  Occupied: wait 0-15 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat (upper limit configurable)
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Timeout

## Slide 43: Break + Question
What are benefits/costs of using or not using beacons?

## Slide 44: Break + Question
What are benefits/costs of using or not using beacons?
  Beacons
    Enable energy savings by designating period with radios off
    Enable structured communication like Guaranteed Slots
    Require some central coordinator within range of all devices
    Tradeoff in inactive period:
      communication latency vs beacon-listening costs
  No beacons
    Enable all devices to be identical (no coordinator needed)
    Require / permit custom communication scheme