## Slide 1: Wireless for the Internet of Things IEEE 802.15.4 – Packets & MAC
CS/ECE 4501
Spring 2023
UVA
[Pannuto, Ghena, Campbell]

## Slide 2: Today’s Goals
IEEE 802.15.4 packet format
Investigate a decade of low power MAC research

## Slide 3: Outline
Packets
MAC Protocols

## Slide 4: Base packet format
Synchronization
  Preamble: four bytes of zeros
    Q: How many chips?
  Start-of-Packet: 0xA7
PHY Header
  One field: length 0-127
  Why still 8 bits?
    Because computers depend on bytes
Q: How long does it take to transmit the preamble?
pollev.com/wiotbc

## Slide 5: MAC frame format
Sequence number
  8-bit monotonically increasing
Addressing fields
  PAN and addresses
  Varies based on frame type
Frame payload
  Depends on frame type
Frame check sequence
  16-bit CRC
Frame control
  Header

## Slide 6: Frame control
Frame type
  Type of payload included
Security enabled
  Packet is encrypted
  (extra 0-14 byte header)
Frame pending
  Fragmented packet
Acknowledgement required
PAN ID compression
  No PAN ID if intra-network
Addressing modes
  Which fields to expect
Why no length field?
Already in prior header

## Slide 7: Frame types - Beacon
Beacon
  Information about the communication structure of this network
  Sent in response to requests from scanning devices
  Sent periodically at start of Superframes (if in use)
    Sent without CSMA/CA
MAC Header
  Source address only, broadcast to everyone
Packet contents
  Superframe details, including Guaranteed Time Slots (if any)
  Pending addresses lists devices for which Coordinator has data

## Slide 8: Frame types - Data
Data
  Data from higher-layer protocols
MAC Header
  Source and/or Destination addresses as necessary
Packet Contents
  Whatever bytes are desired (122 bytes – address sizes)
  May be fragmented across packets

## Slide 9: Frame types – MAC Command
MAC Command
  Various commands for supporting link layer
    Join/leave network
    Change coordinator within network
    Request data from coordinator
    Request Guaranteed Time Slot
MAC Header
  Source and/or Destination addresses as necessary

## Slide 10: Frame types - Acknowledgement
Acknowledgement
  Acknowledges a Data or MAC Command packet
  Not beacons or other acknowledgements
    What happens if acknowledgement isn’t received?
      Packet will be transmitted again
MAC Header
  Repeats Sequence Number of acknowledged packet
  No Source or Destination addresses
Sent TIFS after the packet it is acknowledging (immediately)

## Slide 11: Analysis: maximum goodput
Assume best possible case for data transmission
  122 Bytes per packet
    At 250 kbps -> 3.904 ms
  Plus Inter-frame spacing of 40 symbols
    At 62.5 kBaud -> 0.640 ms
  122 Bytes / 4.544 ms -> 214 kbps
    Compare to BLE advertisements: 9.92 kbps
    Compare to BLE connections: 520 kbps

## Slide 12: Outline
Packets
MAC Protocols

## Slide 13: Enabling full mesh networks
All nodes:
  Can send and receive data
  Route and forward data in the network
Nodes connect with their neighbors
Gateway provides access to other networks/internet
We’re interested in meshes that
  Use low power nodes (battery powered)
  Are low data rate with small packets
802.15.4 provides foundation to build mesh on top
Contention Access Period

## Slide 14: Mesh network layers
PHY Layer
  802.15.4 physical layer
MAC Layer: 802.15.4
  802.15.4 spec gives us the option of implementing our own
  Technically this layer is here, but we generally ignore it
MAC Layer
  Need to allow to TWO low power devices to communicate
  Devices are off most (~99%) of the time
  No assumption of energy asymmetry (as with PAN coordinator or BLE)
Network Layer: Mesh
  Handles organizing the network
  How should packets travel from nodes to the gateway?
  How should packets travel from the gateway to nodes?
  How should packets travel from node to node?
PHY Layer O-QPSK - 2.4 GHz
MAC Layer Low Power
Network Layer Mesh Routing
802.15.4 Contention MAC

## Slide 15: Asynchronous MAC principles
Communication is possible if one device is receiving while other is transmitting
Both devices want to minimize the time they are receiving or transmitting (i.e. their radio is on) to reduce power draw
Devices can only coordinate using the data communication channel (i.e. no out-of-band communication)
  No global synchronization mechanism
Goal: scheme to schedule TX and RX to permit communication while minimizing energy
Energy is paramount, but additional metrics:
  Latency
  Throughput
  Reliability
  Network scale
A
B

## Slide 17
Early 2000s

## Slide 18: Early days of low power sensor nodes
WINSng [Pottie00]
Mica [Hill01]
Rene [Hill99]
Mica2 [Xbow03]
MicaZ [Xbow05]
PC/104 [Cerpa01]
PASTA [Bajura05]
mPlatform[Lymberopoulos07]
WeC [Hill98]
WINS [Rockwell]
Stargate [Intel]
Telos/Tmote
[Polastre05]
Iris [Xbow07]
Tmote Mini
[Sentilla07]
MicaZ Stamp
[Xbow06]
Iris OEM
[Xbow07]

## Slide 19: Low power: multiple year operation using batteries
Pnode = PCPU + PTX + PRX + PSLEEP
EBATT = Pnode * lifetime
Lifetime ⬆️, Pnode⬇️
  PCPU ≫ PSLEEP
  PTX ≫ PSLEEP
  PRX ≫ PSLEEP
  → Minimize compute, TX, RX
  → Maximize sleep

## Slide 20: Low power MAC principles
Communication is possible if one device is receiving while other is transmitting
Devices can only coordinate using the data communication channel (i.e. no out-of-band communication)
  No global synchronization mechanism
Goal: scheme to schedule TX and RX to permit communication while minimizing energy
Energy is paramount, but additional metrics:
  Latency
  Throughput
  Reliability
  Network scale
A
B
Both devices want to minimize the time they are receiving or transmitting (i.e. their radio is on) to reduce power draw

## Slide 21: Low Power Listening (LPL) - B-MAC (2004)
Method:
  Receiver periodically samples the channel
  Transmitter sends a preamble long enough to ensure receiver will detect it
  Upon detection, receiver stays awake to receive transmitted packet
  Receiver ACKs if packet received correctly
CCA
Receiver
Transmitter
Sleep
Sleep
CCA
Sleep
RX
Sleep
Preamble
TX
Sleep
CCA
Sleep
Sleep
Versatile Low Power Media Access for Wireless Sensor Networks. Joseph Polastre, Jason Hill and David Culler. SenSys 2004
CCA
TX ACK
RX ACK

## Slide 22: LPL performance
CCA check interval
  Too small: energy wasted on idle listening
  Too large: energy wasted on transmissions (long preambles)
In general, it’s better to have larger preambles than to check more often!
Sensor sample period – controls the packet rate
Time between listening
(checking if the channel is idle)
Versatile Low Power Media Access for Wireless Sensor Networks. Joseph Polastre, Jason Hill and David Culler. SenSys 2004

## Slide 23: LPL Drawback
CCA
Receiver
Transmitter
Sleep
Sleep
CCA
Sleep
RX
Sleep
Preamble
TX
Sleep
CCA
Sleep
Sleep
CCA
TX ACK
RX ACK
Spend time listening to packets for someone else!
A
B
C
CCA
Receiver
Sleep
Sleep
CCA
Sleep
RX
Sleep
CCA
Sleep
CCA
DROP
A
B
C
Versatile Low Power Media Access for Wireless Sensor Networks. Joseph Polastre, Jason Hill and David Culler. SenSys 2004

## Slide 24: X-MAC: Shorter preambles and destination information
Method
  Transmitter sends a short “I have a packet for this address” packet
  Nodes periodically listen, and ACK if the packet is for them
  Upon receiving the ACK, the transmitter sends full packet
  Receiver successfully receives the full packet.
X-MAC: A Short Preamble MAC Protocol for Duty-Cycled Wireless Sensor Networks. Michael Buettner, Gary V. Yee, Eric Anderson, Richard Han. SenSys 2006.
RX
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
RX
Sleep
Sleep
RX
TX ACK
RX ACK
A
B
TX ACK
RX ACK
TX (DST ID)
TX (DST ID)
TX (DST ID)

## Slide 25: X-MAC: Overhearing node drops out early
RX
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX (DST ID)
TX
Sleep
RX
Sleep
Sleep
RX
TX ACK
RX ACK
A
B
TX ACK
RX ACK
RX
Overhearer
Sleep
Sleep
RX
Sleep
C
TX (DST ID)
TX (DST ID)
X-MAC: A Short Preamble MAC Protocol for Duty-Cycled Wireless Sensor Networks. Michael Buettner, Gary V. Yee, Eric Anderson, Richard Han. SenSys 2006.

## Slide 26: X-MAC: lower power draw than LPL with multiple nearby transmitters
X-MAC: A Short Preamble MAC Protocol for Duty-Cycled Wireless Sensor Networks. Michael Buettner, Gary V. Yee, Eric Anderson, Richard Han. SenSys 2006.

## Slide 27: LPL (B-MAC) and X-MAC are transmitter initiated MAC protocols
Receiving nodes continuously periodically sample the wireless channel
  When they detect a transmission they listen to receive packets
Transmitting nodes are only active when they want to transmit
Receiving nodes prone to unnecessary wakeups
  Have to receive all nearby transmissions to see if the packet happens to be for them
  Unnecessary wakeups lead to increasing receive energy  shorter lifetime
  In general, difficult for receiver to know if it should stay awake or go back to sleep

## Slide 28: Low Power Probing (LPP) is receiver initiated
Method
  Receiver periodically transmits a probe, listens afterward
  Transmitter listens for probe packet from intended recipient
  Transmitter sends packet after receiving the correct probe packet
Koala: Ultra-Low Power Data Retrieval in Wireless Sensor Networks. Razvan Musaloiu-E., Chieh-Jan Mike Liang, Andreas Terzis. IPSN 2008.
TX Probe
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
Sleep
Sleep
RX
TX ACK
A
B
RX ACK
TX Probe
TX Probe
RI-MAC: A Receiver-Initiated Asynchronous Duty Cycle MAC Protocol for Dynamic Traffic Loads in Wireless Sensor Networks. Yanjun Sun, Omer Gurewitz, David B. Johnson. SenSys 2008.

## Slide 29: LPP introduces a new challenge for multiple nodes. What happens with multiple transmitters?
Koala: Ultra-Low Power Data Retrieval in Wireless Sensor Networks. Razvan Musaloiu-E., Chieh-Jan Mike Liang, Andreas Terzis. IPSN 2008.
TX Probe
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
Sleep
Sleep
RX
TX Probe
TX Probe
RI-MAC: A Receiver-Initiated Asynchronous Duty Cycle MAC Protocol for Dynamic Traffic Loads in Wireless Sensor Networks. Yanjun Sun, Omer Gurewitz, David B. Johnson. SenSys 2008.
If multiple transmitters receive a probe, they both transmit, leading to a collision and a lost packet
Receiver is unsure if there actually was a packet, or just noise/interference on the channel
Transmitter
Sleep
TX
Sleep
RX
Collision!!

## Slide 30: A-MAC resolves this with backcast constructive interference
TX Probe
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
Sleep
RX
TX ACK
TX Probe
RX ACK
TX Probe
Method
  Transmitters send an ACK in response to a probe packet
  With multiple transmitters, the ACKs collide, but interfere non-destructively, so the receiver still receives an ACK
  The receiver stays awake to receive a packet, but the packet collides
  The receiver sends a new probe, informing transmitters there was a collision
  Transmitters use CSMA/CA to send packets
Transmitter
Sleep
TX
Sleep
RX
TX ACK
Collision!!
Design and Evaluation of a Versatile and Efficient Receiver-Initiated Link Layer for Low-Power Wireless. Prabal Dutta, Stephen Dawson-Haggerty, Yin Chen, Chieh-Jan Mike Liang, and Andreas Terzis. SenSys 2010.
TX Probe
CCA
TX
CCA
RX
Listen
TX ACK
CCA
RX
TX ACK
TX
RX ACK
RX ACK
Sleep
RX
RX
Listen

## Slide 31: Summary: asynchronous low power MAC protocols
Transmitter initiated protocols
  Receivers periodically sample the channel
  Transmitters transmit sufficiently to ensure recipients heard
  Examples: LPL, X-MAC
  Pros:
    Simple, intuitive
    Can balance TX and RX energy with sample interval
  Cons:
    Receivers prone to false wake-ups
    High idle listening energy costs
Receiver initiated protocols
  Receivers periodically transmit probes
  Transmitters listen for a probe before sending a packet
  Examples: RI-MAC, Koala, A-MAC
  Pros:
    Fixed, small listening energy cost for receivers
  Cons:
    Multiple transmitters leads to collisions

## Slide 32: Mesh network layers
PHY Layer
  802.15.4 physical layer
MAC Layer: 802.15.4
  802.15.4 spec gives us the option of implementing our own
  Technically this layer is here, but we generally ignore it
MAC Layer
  Need to allow to TWO low power devices to communicate
  Devices are off most (~99%) of the time
  No assumption of energy asymmetry (as with PAN coordinator or BLE)
Network Layer: Mesh
  Handles organizing the network
  How should packets travel from nodes to the gateway?
  How should packets travel from the gateway to nodes?
  How should packets travel from node to node?
PHY Layer O-QPSK - 2.4 GHz
MAC Layer Low Power
Network Layer Mesh Routing
802.15.4 Contention MAC