## Slide 1: Wireless for the Internet of Things Introduction to Wireless
CS/ECE 4501
Spring 2023
UVA
[Pannuto, Ghena, Campbell]

## Slide 2: Today’s Goals
Introduce fundamentals of wireless communication
Give you a sense of the intuition behind why we have multiple IoT wireless protocols
Provide a foundation for why different IoT protocols have tradeoffs

## Slide 3: Thinking back…
In the first class we discussed some elements of communication
  Human communication
  I argued many of the same concepts applied to computer communication
I asked “what does this slide say?”
Individually, try to recall the list we created
  What elements are required for communication?
  See what you can remember in two minutes

## Slide 4: Computers face many of the same communication challenges we do
Layers for human communication
  Visual or audio signals (and others)
  Signal vs. noise
  Symbols and sounds
  Alphabet
  Language
  Grammar

## Slide 5: Physical Layer
How bits are transmitted
  Wireless makes this entirely different from wired cases
Important considerations
  Signal strength
  Modulation
  Frequency
application
transport
network
link
physical

## Slide 6: Model of RF communication
Energy that radiates spherically from an antenna
Attenuation with distance
  Density of energy reduces over time, distance
  Signal strength is reduced, errors go up
Three key features
  Inherently broadcast
  Error rates depend on distance
  Spatial reuse of frequencies

## Slide 7: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 8: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 9: Signal strength is measured in decibels
Power is measured in watts or dBw or dBm
dBm is most relevant to the IoT domain
  0 dBm equals 1 mW transmit power
  Example
    Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
    Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
Rules of thumb: +3 dB is double the power, 10 dB is 10x power

## Slide 10: Signal strength varies significantly across technologies
Bluetooth Low Energy (local area)
  nRF52840 transmit power: 8 dBm (6.31 mW)
  nRF52840 receive sensitivity: -95 dBm (316.2 fW)
LoRa (wide area)
  SX127X LoRa transmit power: 20 dBm (100 mW)
  SX127X LoRa receive sensitivity: -148 dBm (1.6 attoWatt)

## Slide 11: Propagation degrades RF signals
Attenuation in free space
  Signals get weaker as they travel over long distances
  Signal spreads out  free space path loss

## Slide 12: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
6.31 mW

## Slide 13: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
.25 m

## Slide 14: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
1 m

## Slide 15: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
2 m

## Slide 16: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
2 m
0.00016 mW
46 dB path loss!

## Slide 17: Okay.. So what’s the limit?
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
8 dBm – -95 dBm = 103 dB link margin
For FSPL alone for a 2.4 GHz signal, 103 dB is 1,400 m!
Bluetooth does not go 1.4 km…

## Slide 18: Propagation is one thing that degrades RF signals
Attenuation in free space
  Signals get weaker as they travel over long distances
  Signal spreads out  free space path loss
Important: distance is NOT the only signal strength loss
  Free space path loss calculation will not give you accurate range for a signal
Many other factors (e.g. physical obstacles, interference, reflections,…)
  Precise quantitative details are in the EE domain
  We will use quantitative examples to develop qualitative instincts in this class

## Slide 19: ITU model for Indoor Attenuation
Models like this are more trustworthy less bad than FSPL
  https://en.wikipedia.org/wiki/ITU_model_for_indoor_attenuation
Notes: ITU: International Telecommunication Union

## Slide 20: Lower received energy increases error rates
More Errors
Fewer Errors
More Energy Received
Less Energy Received
BER: Bit Error Rate
Odds that a transmitted bit will be received incorrectly

## Slide 21: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 22: Frequency separation enables different wireless technologies to operate simultaneously

## Slide 23: Wireless spectrum is limited...and valuable
FCC auctioned off 3.5 GHz spectrum in August 2020
  70 MHz
  $4.6 billion

## Slide 24: Unlicensed bands are where the IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why?
No interference from other users!

## Slide 25: Different technologies use spectrum in different ways
How spectrum is used affects: cost, robustness, throughput, distance, …
  We will talk about how each technology uses spectrum, and implications
This graphic shows how BLE and WiFi interoperate; more on this next week

## Slide 26: One Example / Bluetooth Preview: Frequency Hopping Spread Spectrum (FHSS)
Transmitter hops through a sequence of transmit channels
  Spend some “dwell time” on each channel before hopping again
  Receiver must know the hopping pattern
Avoid causing or receiving prolonged interference

## Slide 27: Sidebar: inventor of FHSS – Hedy Lamarr
Actress and Inventor
  Designed FHSS with George Antheil during WWII
  Idea: torpedo control can’t be easily jammed if it jumps around
https://en.wikipedia.org/wiki/Hedy_Lamarr#Inventor

## Slide 28: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 29: Computers face many of the same communication challenges we do
Layers for human communication
  Visual or audio signals (and others)
  Signal vs. noise
  Symbols and sounds
  Alphabet
  Language
  Grammar

## Slide 30: Computers face many of the same communication challenges we do
Layers for human communication
  Visual or audio signals (and others)  EM spectrum waves
  Signal vs. noise  signal strength
  Symbols and sounds
  Alphabet
  Language  roughly akin to channel/frequency
  Grammar

## Slide 31: Computers face many of the same communication challenges we do
Layers for human communication
  Visual or audio signals (and others)  EM spectrum waves
  Signal vs. noise  signal strength
  Symbols and sounds  modulation
  Alphabet
  Language  roughly akin to channel/frequency
  Grammar

## Slide 32: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 33: Modulation
Encoding signal data in an analog “carrier” signal
  Carrier signal defines the frequency
  Modulation scheme + data define bandwidth required

## Slide 34: Modulation: On-Off keying
Intuition: when carrier is present  1, no carrier  0
Simple
Spectrum frugal
Issues
  Desynchronization with runs of same value
  Susceptible to noise

## Slide 35: Modulation types
Encoding binary data on a signal
Amplitude-shift Keying (ASK)
  Modify amplitude of carrier signal
  On-Off Keying (OOK) is an extreme example
Frequency-shift Keying (FSK)
  Modify frequency of carrier signal

## Slide 36: Modulation types
Phase-shift keying (PSK)
  Modify phase of carrier signal
  Usually differential: the change signifies data
More complicated possibilities exist
  QAM (Quadrature Amplitude Modulation) combines amplitude and phase shift keying
    Allows for more than one bit per “symbol”

## Slide 37: Modulation tradeoffs
Various tradeoffs between different modulation schemes
  Bandwidth requirements, transceiver hardware, immunity to noise, etc.
ASK (amplitude) is simple but susceptible to noise
  Noise exists in the real world
FSK (frequency) is relatively simple and robust to noise, but uses more bandwidth
  Bandwidth is limited, but still commonly used
PSK (phase) energy efficient and robust, but more complex hardware
  More expensive hardware, but very commonly used

## Slide 38: Outline
Physical Layer
Data Link Layer

## Slide 39: Data Link Layer
Framing
  Combine arbitrary bits into a “packet” of data
Logical link control
  Manage transfer between transmitter and receiver
  Error detection and correction
Media access
  Controlling which device gets to transmit next
Inherently coupled to PHY and its decisions

## Slide 40: Framing
Typical packet structure
  Preamble - Existence of packet and synchronization of clocks
  Header - Addresses, Type, Length
  Data - Payload plus higher layer headers (e.g. IP packet)
  Trailer - Padding, CRC
Wireless considerations
  Control information for Physical Layer
  Ensure robustness for header
  Explicit multi-hop routing
  Possibly different data rates for different parts of packet
Preamble | Destination Address | Source Address | Type and Length | Data | CRC

## Slide 41: Error control: detection and recovery
Detection: only detect errors
  Make sure corrupted packets get discarded
  Cyclical Redundancy Checks
    Detect single bit errors
    Detect “burst” errors of several contiguous bits
Recovery: also try to recover from small bit errors
  Forward error correction
  Retransmissions
  Far more important for wireless because the cost of transmission is higher

## Slide 42: Medium Access Control
How does a network determine which transmitter gets to transmit?
Remember: the wireless medium is inherently broadcast
  Two simultaneous transmitters may lose both packets

## Slide 43: Thinking back…
You came up with a MAC protocol!
What was it?

## Slide 44: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”

## Slide 45: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Eye contact (or raise hand) → out-of-band communication
Wait until it’s quiet for some time → carrier sense multiple access
Strict turn order → time division multiple access
Just speak and hope it works → ALOHA
Everybody sing at different tones → frequency division multiple access (stretching the metaphor)
Everyone speak in different languages → code division multiple access
Others?

## Slide 46: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 47: ALOHA
ALOHAnet (1971)
  University of Hawaii – Norman Abramson
  First demonstration of wireless packet network
Rules
  If you have data to send, send it
Two (or more) simultaneous transmissions will collide and be lost
  Wait a duration of time for an acknowledgement
  If transmission was lost, try sending again “later”
    Want some kind of exponential backoff scheme with entropy here

## Slide 48: Packet collisions
Each packet transmission has a window of vulnerability
  Twice the on-air duration of a packet
  Transmissions during the packet are bad
  Transmissions before packet can also be bad
My blessed device
Interferer
time
My blessed device
Interferer
time

## Slide 49: Slotted ALOHA
Split time into synchronized “slots”
Any device can transmit whenever it has data
  But it must transmit at the start of a slot
  And its transmission cannot be longer than a slot
  Removes half of the possibilities for collisions!
    At the cost of some synchronization method
time

## Slide 50: ALOHA throughput
It can be shown that traffic maxes out at
  ALOHA: 18.4%
  Slotted ALOHA: 36.8%
Assuming Poisson distribution of transmission attempts
Slotted throughput is double because the “before” collisions can no longer occur
(transmission events / time frame)

## Slide 51: Capture effect
Actually, two packets at once isn’t always a total loss
  The louder packet can still sometimes be heard if loud enough
How much louder?
  Ballpark 12-14 dB
When does this work?
  Depends on the radio hardware
  Louder packet first almost always works
  Louder packet second sometimes works

## Slide 52: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 53: CSMA/CA – Carrier Sense Multiple Access with Collision Avoidance
First listen for a duration and determine if anyone is transmitting
  If idle, you can transmit
  If busy, wait and try again later
“listen before send”
Can be combined with notion of slotting
  If current slot is idle, transmit in next slot
  If current slot is busy, follow some algorithm to try again later

## Slide 54: CSMA/CD – CSMA with Collision Detection
Detect collisions during your own transmission
  Works great on wired mediums (Ethernet, I2C)
Somewhere between challenging and impossible for wireless
  Transmit and receive are usually the same antenna
  Receiving while transmitting would be drowned out by transmission
    Remember: nrf52840 TX at 8 dBm and RX at -95 dBm

## Slide 55: Hidden terminal problem
Device A
Device B
Device C

## Slide 56: CSMA with RTS/CTS
Hidden terminal problem means that two transmitters might never be able to detect each other’s transmissions
A partial solution
  When channel is idle, transmitter sends a short Request To Send (RTS)
  Receiver will send a Clear To Send (CTS) to only one node at a time
  RTS collisions are faster and less wasteful than hidden terminal collisions
  Downside: overhead is high for waiting for CTS when contention is low

## Slide 57: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 58: Contention-free access control protocols
Goal: split up communication such that devices will not conflict
Can be predetermined or reservation-based
  Devices might request to join the schedule and be given a slot
    Devices lose their slot if it goes unused for some amount of time
    Reservations often occur during a dedicated CSMA contention slot
  Assignment of schedules can be complicated
Really efficient at creating a high-throughput network
  Assuming they are all following the same protocol
  Otherwise, interference can be very problematic

## Slide 59: FDMA – Frequency Division Multiple Access
Split transmissions in frequency
  Different carrier frequencies are independent
  Fundamentally how RF spectrum is split
Technically, each device uses a separate, fixed frequency
  Walkie-talkies
Conceptually, how RF channels work
  WiFi networks pick different bands
  802.15.4 picks a channel to communicate on

## Slide 60: TDMA – Time Division Multiple Access
Split transmissions in time
  Devices share the same channel
Splits time into fixed-length windows
  Each device is assigned one or more windows
  Can build a priority system here with uneven split among devices
Requires synchronization between devices
  Often devices must listen periodically to resynchronize
  Less efficient use of slots reduce synchronization
    Large guard windows. E.g. 1.5 second slot for a 1 second transmission

## Slide 61: CDMA – Code Division Multiple Access
Split transmissions in ‘codes’
  Not new; original applications in radar and early satellite communications
Analogy: Multiple speakers in the same room all in different languages
  [The human brain is crazy good at ignoring what it doesn’t understand ]
Requires signal power coordination
  [everyone needs to speak ~the same volume]
  Can be hard in uncontrolled / dynamic environments
Also can be more performant with highly synchronized clocks
  i.e. if the code clock is known to both devices; intractable in mobile settings

## Slide 62: Real-world protocol access control
ALOHA
  BLE advertisements
  Unlicensed LPWANs: Sigfox, LoRaWAN
CSMA
  WiFi (slotted, CSMA/CA)
  802.15.4
TDMA
  BLE connections
  Cellular LPWANs: LTE-M and NB-IoT
CDMA
  Most modern cellular networks