## Slide 1: CS6456: Graduate Operating Systems
Brad Campbell – bradjc@virginia.edu
https://www.cs.virginia.edu/~bjc8c/class/cs6456-f19/
Slides modified from CS162 at UCB

## Slide 2: Recall: What is an OS?
Referee
  Resource sharing, protection, isolation
Illusionist: clean, easy to use abstractions
    Infinite memory, dedicated machine
    Higher level objects: files, users, messages
    Masking limitations, virtualization
Glue: Common Services
    Storage
    Window system
    Networking
    Authorization

## Slide 3: OS Bottom Line: Run Programs
Load instruction and data segments of executable file into memory
Create stack and heap
“Transfer control to program”
Provide services to program
While protecting OS and program
int main()
{ … ;
}
editor
Program Source
foo.c
Load & Execute
Memory
PC:
Processor
registers
0x000…
0xFFF…
instructions
data
heap
stack
OS
compiler
Executable
a.out
data
instructions

## Slide 4: Four Fundamental OS Concepts
Thread: Execution Context
  Program Counter, Registers, Execution Flags, Stack
Address space (with translation)
  Program's view of memory is distinct from physical machine
Process: an instance of a running program
  Address Space + One or more Threads
Dual mode operation / Protection
  Only the “system” can access certain resources
  Combined with translation, isolates programs from each other

## Slide 5: Threads of Control
Definition: A single, unique execution context
  Program counter, registers, stack
A thread is executing on a processor when it is resident in that processor's registers
Registers hold the root state of the thread:
  The rest is "in memory"
  Including program counter – the currently executing instruction
Registers point to thread state in memory:
  Stack pointer to the top of the thread's (own) stack

## Slide 6: Multiprogramming - Multiple Threads of Control
OS
Thrd. 1
Thrd. 2
Thrd. n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack

## Slide 7: Illusion of Multiple Processors
Multiple threads: Multiplex hardware in time
Contents of virtual core (thread):
  Program counter, stack pointer
  Registers
Where is it?
  On the real (physical) core, or
  Saved in memory – called the Thread Control Block (TCB)
vCPU3
vCPU2
vCPU1
Shared Memory
vCPU1
vCPU2
vCPU3
vCPU1
vCPU2
Time

## Slide 8: Very Simple Multiprogramming
All vCPU's share non-CPU resources
  Memory, I/O Devices
Each thread can read/write data of others
Threads can overwrite OS functions
Unusable? No. This approach is used in
  Embedded applications (but not all!)
  MacOS 1-9/Windows 3.1 (switch only with voluntary yield)
  Windows 95-ME (switch with yield or timer)

## Slide 9: Four Fundamental OS Concepts
Thread: Execution Context
  Program Counter, Registers, Execution Flags, Stack
Address space (with translation)
  Program's view of memory is distinct from physical machine
Process: an instance of a running program
  Address Space + One or more Threads
Dual mode operation / Protection
  Only the “system” can access certain resources
  Combined with translation, isolates programs from each other

## Slide 10: Second OS Concept: Address Space
Definition: Set of accessible addresses and the state associated with them
  232 = ~4 billion on a 32-bit machine
What happens when you read or write to an address?
  Perhaps nothing
  Perhaps acts like regular memory
  Perhaps causes I/O operation
    (Memory-mapped I/O)
  Crash
  Communicate with another program
0x000…
0xFFF…
code
Static Data
heap
stack

## Slide 11: Address Space Translation
Program operates in an address space that is distinct from the physical memory space of the machine
Processor
Memory
0x000…
0xFFF…
translator
“virtual address”
“physical address”
Gives every process the whole address range
Breaks memory into pages (~4K chunks)
Allows unallocated "holes" and other tricks

## Slide 12: Four Fundamental OS Concepts
Thread: Execution Context
  Program Counter, Registers, Execution Flags, Stack
Address space (with translation)
  Program's view of memory is distinct from physical machine
Process: an instance of a running program
  Address Space + One or more Threads
Dual mode operation / Protection
  Only the “system” can access certain resources
  Combined with translation, isolates programs from each other

## Slide 13: The Process
Definition: execution environment with restricted rights
  Address Space with One or More Threads
  Owns memory (address space)
  Owns file descriptors, file system context, …
  Encapsulate one or more threads sharing process resources
Why processes?
  Protected from each other!
  OS protected from them
Tradeoff: protection vs. efficiency
    Threads more efficient than processes (more later)
Application: one or more processes

## Slide 14: Single and Multithreaded Processes
Threads encapsulate concurrency: “Active” component
Address spaces encapsulate protection: “Passive” part
  Keeps buggy program from trashing the system
Why have multiple threads per address space?

## Slide 15: Protection
Why?
  Reliability: buggy programs only hurt themselves
  Security and privacy: trust programs less
  Fairness: enforce shares of disk, CPU
Mechanisms:
  Address translation: address space only contains its own data
  Privileged instructions, registers
  Syscall processing (e.g., enforce file access rights)

## Slide 16: Four Fundamental OS Concepts
Thread: Execution Context
  Program Counter, Registers, Execution Flags, Stack
Address space (with translation)
  Program's view of memory is distinct from physical machine
Process: an instance of a running program
  Address Space + One or more Threads
Dual mode operation / Protection
  Only the “system” can access certain resources
  Combined with translation, isolates programs from each other

## Slide 17: Dual Mode Operation: HW Support
1 bit of state (user/kernel mode bit)
  Always?
Certain actions only permitted in kernel mode
User->Kernel mode sets kernel mode, saves user PC
  Only transition to OS-designated addresses
  OS can save the rest of the user state if necessary
Kernel->User mode sets user mode, restores user PC

## Slide 18: UNIX Structure

## Slide 19: 3 Types of U→K Mode Switches
System Call (syscall)
  "Function call" into the kernel
  Example: exit, read
  Kernel reads syscall id # and arguments from user registers
Interrupt
  External asynchronous events: Timer, I/O
Trap or Exception
  Special event in process
  Protection violation (segfault), divide by zero
All 3 are an implicit transfer of control

## Slide 20: Where do mode transfers go?
Cannot let user program specify (why?)
Solution: Interrupt Vector
interrupt number (i)
intrpHandler_i () {
…
}
Address and properties of each interrupt handler

## Slide 21: Implementing Safe Kernel Mode Transfers
Carefully constructed kernel code packs up the user process state and sets it aside
Must handle weird/buggy/malicious user state
  Syscalls with null pointers
  Return instruction out of bounds
  User stack pointer out of bounds
Should be impossible for buggy or malicious user program to cause the kernel to corrupt itself
User program should not know interrupt has occurred (transparency)
  Can a user program find out?

## Slide 22: The Kernel Stack
Two-stack model
  Each OS thread has kernel stack (located in kernel memory) plus user stack (located in user memory)
Place to save user registers during interrupt

## Slide 23: Before Interrupt

## Slide 24: During Interrupt

## Slide 25: How do we take interrupts safely?
Interrupt vector
  Limited number of entry points into kernel
Kernel interrupt stack
  Handler works regardless of state of user code
Interrupt masking
  Handler is non-blocking
Atomic transfer of control
  “Single instruction”-like to change:
    Program counter
    Stack pointer
    Memory protection
    Kernel/user mode
Transparent restartable execution
  User program does not know interrupt occurred

## Slide 26: Kernel System Call Handler
Vector through well-defined syscall entry points!
  Table mapping system call number to handler
Locate arguments
  In registers or on user (!) stack
Copy arguments
  From user memory into kernel memory – carefully checking locations!
  Protect kernel from malicious code evading checks
Validate arguments
  Protect kernel from errors in user code
Copy results back
  Into user memory – carefully checking locations!

## Slide 27: Example: Context switch and interrupt
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
xxxx…
uPC
regs
sysmode
…
1
PC
Start: OS running

## Slide 28: About to Switch
Privileged Inst: set special registers
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
0001…
uPC
regs
sysmode
…
1
PC
00FF…

## Slide 29: User Code Running
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
xxxx…
uPC
regs
sysmode
…
0
PC

## Slide 30: Handling Interrupt
Save registers and set up system stack
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
0000 1234
uPC
regs
sysmode
…
1
PC
00FF…
IntrpVector[i]

## Slide 31: How do we switch between processes?
We already have all the necessary machinery!
Just requires two mode transfers

## Slide 32: Representing Processes: PCB
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
Base
1000 …
1100 …
Bound
xxxxxx
uPC
sysmode
…
0
PC
0000…
FFFF…
0000 100
RTU
1000 …
1100 …
0000 1234
regs
00FF…

## Slide 33: Process Control Block
Kernel representation of each process
  Status (running, ready, blocked)
  Register state (if not running)
  Thread control block(s)
  Process ID
  Execution time
  Memory translations
Scheduler maintains a data structure of PCBs

## Slide 34: Scheduler
Scheduling: Mechanism for deciding which processes/threads receive the CPU
Lots of different scheduling policies provide …
  Fairness or
  Realtime guarantees or
  Latency optimization or ..
if ( readyProcesses(PCBs) ) {
nextPCB = selectProcess(PCBs);
run( nextPCB );
} else {
run_idle_process();
}

## Slide 35: Process Operations
Question: How does a process start?
Processes need to manipulate other processes:
  Start a new process
  Exit
  Wait for another process to terminate
Can a process start another without OS help?
  A thread, yes, but not another process
  Process must use syscalls to interact with kernel

## Slide 36: What does "syscall" really mean?
Application programmers generally don’t write syscalls directly
Can’t in C without inline assembly, etc.
Instead, OS libraries do this on our behalf

## Slide 37: OS Run-Time Library
OS
Proc 1
Proc 2
Proc n
…
OS
Appln
login
Window Manager
…
OS library
OS library
OS library

## Slide 38: A Narrow Waist
Compilers
Web Servers
Web Browsers
Databases
Email
Word Processing
Portable OS Library
System Call
Interface
Portable OS Kernel
Platform support, Device Drivers
x86
ARM
PowerPC
Ethernet (1Gbs/10Gbs)
802.11 a/g/n/ac
SCSI
Thunderbolt
Graphics
PCI
Hardware
Software
System
User
OS
Application / Service

## Slide 39: POSIX/Unix
Portable Operating System Interface [X?]
Defines “Unix”, derived from AT&T Unix
  Created to bring order to many Unix-derived OSs
Interface for application programmers (mostly)
Notes: http://stallman.org/articles/posix.html

## Slide 40: Example: pid.c
#include <stdlib.h>
#include <stdio.h>
#include <unistd.h>
#include <sys/types.h>
int main(int argc, char *argv[]) {
/* get current process’s PID */
pid_t pid = getpid();
printf(“My pid: %d\n”, (int) pid);
exit(0);
}

## Slide 41: Process Management
Syscalls:
  fork – copy the current process
  exec – change the program being run by the current process
  wait – wait for a process to finish
  kill – send a signal (interrupt-like notification) to another process
  sigaction – set handlers for signals
Lot of legacy here.
  Further reading: https://www.microsoft.com/en-us/research/uploads/prod/2019/04/fork-hotos19.pdf

## Slide 42: Creating Processes
pid_t fork(); -- copy the current process
  New process has different pid
Return value from fork(): pid (int)
  When > 0:
    Running in (original) Parent process
    return value is pid of new child
  When = 0:
    Running in new Child process
  When < 0:
    Error! Must handle somehow
    Running in original process
State of original process duplicated in both Parent and Child!
  Memory, File Descriptors (covered later), etc…

## Slide 43: What happens when we use fork?
OS
Child
Parent
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
Base
1000 …
1100 …
Bound
0000…
uPC
sysmode
…
1
PC
0000…
FFFF…
1000 …
1100 …
0000 1234
regs
00FF…
3000 …
3080 …
0000 1234
regs
00FF…

## Slide 44: Example: fork1.c
#include <stdlib.h>
#include <stdio.h>
#include <unistd.h>
#include <sys/types.h>
int main(int argc, char *argv[]) {
pid_t cpid, mypid;
pid_t pid = getpid(); /* get current processes PID */
printf("Parent pid: %d\n", pid);
cpid = fork();
if (cpid > 0) { /* Parent Process */
mypid = getpid();
printf("[%d] parent of [%d]\n", mypid, cpid);
} else if (cpid == 0) { /* Child Process */
mypid = getpid();
printf("[%d] child\n", mypid);
} else {
perror("Fork failed");
}
}

## Slide 45: Process Management
fork – copy the current process
exec – change the program being run by the current process
wait – wait for a process to finish
kill – send a signal (interrupt-like notification) to another process
sigaction – set handlers for signals

## Slide 46: fork2.c
int status;
pid_t tcpid;
…
cpid = fork();
if (cpid > 0) { /* Parent Process */
mypid = getpid();
printf("[%d] parent of [%d]\n", mypid, cpid);
tcpid = wait(&status);
printf("[%d] bye %d(%d)\n", mypid, tcpid, status);
} else if (cpid == 0) { /* Child Process */
mypid = getpid();
printf("[%d] child\n", mypid);
}
…

## Slide 47: Process Management
fork – copy the current process
exec – change the program being run by the current process
wait – wait for a process to finish
kill – send a signal (interrupt-like notification) to another process
sigaction – set handlers for signals

## Slide 48: fork3.c
…
cpid = fork();
if (cpid > 0) { /* Parent Process */
tcpid = wait(&status);
} else if (cpid == 0) { /* Child Process */
char *args[] = {“ls”, “-l”, NULL};
execv(“/bin/ls”, args);
/* execv doesn’t return when it works.
So, if we got here, it failed! */
perror(“execv”);
exit(1);
}
…

## Slide 49: Process Management

## Slide 50: Shell
Job control system
  Allows user to create/manage applications to do tasks
  User’s wrapper around process management functions
  Windows, OS X, Linux all have shells

## Slide 51: Process Management
fork – copy the current process
exec – change the program being run by the current process
wait – wait for a process to finish
kill – send a signal (interrupt-like notification) to another process
sigaction – set handlers for signals

## Slide 52: inf_loop.c
#include <stdlib.h>
#include <stdio.h>
#include <sys/types.h>
#include <unistd.h>
#include <signal.h>
void signal_callback_handler(int signum) {
printf(“Caught signal!\n”);
exit(1);
}
int main() {
struct sigaction sa;
sa.sa_flags = 0;
sigemptyset(&sa.sa_mask);
sa.sa_handler = signal_callback_handler;
sigaction(SIGINT, &sa, NULL);
while (1) {}
}

## Slide 53: Common POSIX Signals
SIGINT – control-C
SIGTERM – default for kill shell command
SIGSTP – control-Z (default action: stop process)
SIGKILL, SIGSTOP – terminate/stop process
  Can’t be changed with sigaction
  Why?

## Slide 55: Multiplexing Processes
Process Control
Block
Snapshot of each process in its PCB
  Only one active at a time (per core…)
Give out CPU to different processes
  Scheduling
  Policy Decision
Give out non-CPU resources
  Memory/IO
  Another policy decision

## Slide 56: Context Switch
Overhead!

## Slide 57: Lifecycle of a Process
As a process executes, it changes state:
  new: being created
  ready: waiting to run
  running: instructions executing on the CPU
  waiting: waiting for some event to occur (e.g., keypress)
  terminated: finished execution

## Slide 58: Scheduling: All About Queues
PCBs move from queue to queue
Scheduling: which order to remove from queue

## Slide 59: Modern Processes: Multiple Threads
Thread: execution stream within a process
  Used to be called "lightweight processes"
  Shares address space with other threads belonging to the same process
Why separate concepts of threads and processes?
  Threads: Concurrency
  Processes: Protection

## Slide 60: So does the OS schedule processes or threads?
Usually it's threads (e.g., in Linux)
One point to notice: switching threads vs. switching processes incurs different costs:
  Switch threads: Save/restore registers
  Switch processes: Change active address space too!
    Expensive
    Disrupts caching

## Slide 61: Thread vs. Process State
Process-wide state:
  Memory contents (global variables, heap)
  I/O bookkeeping
Thread-"private" state:
  CPU registers including program counter
  Execution stack
  Kept in Thread Control Block

## Slide 62: Execution Stack Review
Stack holds temporary results
Used to implement recursion
A(int tmp) {
if (tmp<2)
B();
printf(tmp);
}
B() {
C();
}
C() {
A(2);
}
A(1);
A: tmp=2
ret=C+1
Stack Growth
A: tmp=1
ret=exit
B: ret=A+2
C: ret=b+1
Stack
Pointer

## Slide 63: Shared vs. Per-Thread State

## Slide 64: Memory Footprint: Two Threads
Two sets of CPU registers
Two sets of Stacks
Issues:
  How do we position stacks relative to each other?
  What maximum size should we choose for the stacks?
  What happens if threads violate this?
  How might you catch violations?
Code
Global Data
Heap
Stack 1
Stack 2
Address Space

## Slide 65: Threads Motivation
Back to Jeff Dean's "Numbers everyone should know"
Handle I/O in separate thread, avoid blocking other progress

## Slide 66: Example for Threads
Imagine the following program:
main() {
…
ReadLargeFile(“pi.txt”);
RenderUserInterface();
}
What is the behavior here?
  Still respond to user input
  While reading file in the background

## Slide 67: Dispatch Loop
Loop {
RunThread();
ChooseNextThread();
SaveStateOfCPU(curTCB);
LoadStateOfCPU(newTCB);
}
Conceptually all the OS executes
Infinite Loop
  When would we ever "exit?"
  Can we assume some thread is always ready?

## Slide 68: Dispatch Loop
Loop {
RunThread();
ChooseNextThread();
SaveStateOfCPU(curTCB);
LoadStateOfCPU(newTCB);
}
How to run a new thread?
  Load thread's registers into CPU
  Load its environment (address space, if in different process)
  Jump to thread's PC
How does dispatch loop get control again?
  Thread returns control voluntarily – yield, I/O
  External events: thread is preempted

## Slide 69: Thread switching
I/O – e.g. keypress
Waiting for a signal from another thread
  Thread makes system call to wait
Thread executes thread_yield()
  Relinquishes CPU but puts calling thread back on ready queue

## Slide 70: Stack for Yielding Thread
Cyan = User Stack; Red = Kernel Stack
run_new_thread() {
newThread = PickNewThread();
switch(curThread, newThread);
ThreadHouseKeeping(); /* Do any cleanup */
}
yield
ComputePI
Stack growth
run_new_thread
kernel_yield
Trap to OS
switch

## Slide 71: The Context Switch Itself
Switch(tCur,tNew) {
/* Unload old thread */
TCB[tCur].regs.r7 = CPU.r7;
…
TCB[tCur].regs.r0 = CPU.r0;
TCB[tCur].regs.sp = CPU.sp;
TCB[tCur].regs.retpc = CPU.retpc; /*return addr*/
/* Load and execute new thread */
CPU.r7 = TCB[tNew].regs.r7;
…
CPU.r0 = TCB[tNew].regs.r0;
CPU.sp = TCB[tNew].regs.sp;
CPU.retpc = TCB[tNew].regs.retpc;
return; /* Return to CPU.retpc */
}

## Slide 72: Summary
Variety of process management syscalls
  fork, exec, wait, kill, sigaction
Process consists of two pieces
  Address Space (Protection)
  One or more threads (Concurrency)
Scheduling: Threads move between queues
Threads: multiple stacks per address space
  Context switch: Save/Restore registers, "return" from new thread's switch routine